ASSIGNMENT – 2
Advanced Programming Lab
Name: Utsav Balar
Roll.no. t24cs003

Objective:
Assignments on Familiarisation microcontroller board (Arduino/ Raspberry Pi) Assignment on sensors and how to interface them with the microcontroller board, data acquisition and processing of GSR data

### Overview of the Arduino UNO:
The Arduino UNO is a microcontroller board built around the ATmega328P. It features 14 digital input/output pins, of which 6 support PWM outputs, as well as 6 analog inputs, a 16 MHz ceramic resonator, a USB port, a power jack, an ICSP header, and a reset button. The board is equipped to handle all the essentials for running the microcontroller; you can power it either through a USB connection to a computer or with an AC-to-DC adapter or battery. The Arduino UNO is an open-source hardware platform developed by Arduino.cc, initially released in 2010. It supports integration with a variety of expansion shields and circuits, thanks to its digital and analog I/O pins. It has a USB-B connector for programming with the Arduino IDE. The board can run on power supplied through USB or a barrel jack, accommodating input voltages from 7 to 20 volts. The design is open-source and distributed under the Creative Commons Attribution Share-Alike 2.5 license, with layout and production files available on the Arduino website.
###
### Key Specifications (from UNO R1 to R3):
1. Microcontroller: Microchip ATmega328P (8-bit AVR core)
2. Clock Speed: 16 MHz on the board, with a max of 20 MHz at 5V for the IC
3. Memory:
4. Flash: 32 KB (0.5 KB used by the bootloader)
5. SRAM: 2 KB
6. EEPROM: 1 KB
7. Peripherals:
8. 1 UART (default configured as an 8N1 UART)
9. 1 SPI
10. 1 I²C
11. Operating Voltage: 5V
12. Digital I/O Pins: 14
13. PWM Pins: 6 (pins 3, 5, 6, 9, 10, 11)
14. Analog Input Pins: 6
15. DC Current Limits:
16. Per I/O Pin: 20 mA
17. 3.3V Pin: 50 mA
18. Physical Characteristics:
19. Size: 68.6 mm x 53.4 mm
20. Weight: 25 g
21. ICSP Header: Yes
22. Power Options:
23. USB Connector: Supplies power in the range of 4.75 to 5.25 volts. Official boards use a USB-B connector, though third-party variations might feature microUSB, miniUSB, or USB-C.
24. Barrel Jack: Supports 6 to 20 volts, with 7 to 12 volts recommended. Third-party boards may have different maximum voltages depending on the voltage regulator used.
25. VIN Pin: Accepts similar voltage as the barrel jack. However, it lacks reverse voltage protection, so an external diode is necessary if using both the VIN pin and barrel jack simultaneously.
### Applications of the Arduino UNO:
1. Home Automation: Automate lighting, temperature control, security systems, and energy management. For example, using IR sensors for automatic light control.
2. Robotics: Build autonomous robots equipped with sensors, motors, and controllers.
3. Smart Gardening: Develop systems for automated plant care, such as moisture-based irrigation.
4. IoT Devices: Create Internet of Things devices for various smart applications.
5. Wearable Technology: Design and implement wearable electronic gadgets.
6. Control and Measurement: Useful in advanced scenarios like Industry 4.0, industrial cyber-physical systems (ICPSs), and smart grid applications.
7. Miscellaneous Uses: Includes applications in security, embedded systems, digital electronics, weighing systems, parking counters, medical instrumentation, and countdown timers for traffic lights

Arduino code to blink a LED :

void setup() { / // initialize digital pin LED_BUILTIN as an output. / pinMode(LED_BUILTIN, OUTPUT); / } / // the loop function runs over and over again forever / void loop() { / digitalWrite(LED_BUILTIN, HIGH); // turn the LED on (HIGH is the voltage level) / delay(1000); // wait for a second / digitalWrite(LED_BUILTIN, LOW); // turn the LED off by making the voltage LOW / delay(1000); // wait for a second / }

* Data acquisition and processing of GSR data

code.ino:
// Pin configuration
constexpr uint8_t GSR_PIN = A0;

const int sensorValue = 0;
const int gsrAverage = 0;
const float V_supply = 5.0;
const float R_fixed = 10000;
void setup() {
    Serial.begin(9600);
}

void loop() {
    constexpr size_t NUM_READINGS = 10;
    long sum = 0;

    for (size_t i = 0; i < NUM_READINGS; ++i) {
        sensorValue = analogRead(GSR_PIN);
        sum += sensorValue;
        delay(5);
    }

    gsrAverage = static_cast<int>(sum / NUM_READINGS);

    long V_out = (sensorValue * V_supply) / 1023.0;
    long g_sensor_R = R_fixed * ((V_supply / V_out) - 1);
    Serial.println("Human Resistance: ");
    Serial.print(g_sensor_R);
    Serial.println("GSR Average: ")
    Serial.println(gsrAverage);

    delay(500);
}

Output after taking 100 samples:

Fig: Simulated GSR readings over time

Fig: Output from the sensor